## Slide 1
Chapter 4: Doppler Imaging Concepts Examination Review for Ultrasound: Sonographic Principles and Instrumentation, 2nd ed. Steven M. Penny, MA, RT(R), RDMS Traci B. Fox, EdD, RT(R), RDMS, RVT

## Slide 2: Hemodynamics

## Slide 3: Types of Energy
Hemodynamics is the study of blood flow through the blood vessels of the body.
It is because of a difference in fluid energy that there is flow through a blood vessel.
This difference in fluid energy is called an energy gradient.
It is equal to E1 − E2, where E1 is the energy at the beginning of the vessel and E2 is the energy at the end of the vessel.
Without an energy gradient, there is no flow.

## Slide 4: Types of Energy
Pressure energy is the driving force of the blood through the blood vessels.
It is the pumping of the heart that provides the necessary potential energy at the beginning of the system.
Subsequently, this potential energy is converted into kinetic energy in the form of flowing blood within the blood vessels.
Hydrostatic pressure, also known as gravitational potential energy, describes the relationship between gravity, the density of the blood, and the distance between an arbitrary reference point (usually the heart).

## Slide 5: Types of Energy
As blood flows through a vessel, it loses energy.
Viscous energy is a form of energy loss. It is produced when kinetic energy is converted to heat as a result of friction.
Blood also undergoes inertial losses, which occur when blood vessels divide, forcing the blood flow to change direction.
Inertia is described by Newton’s first law, which essentially states that an object at rest stays at rest and an object in motion stays in motion, unless acted on by an outside force.
Each time blood changes direction, there is an energy loss related to inertia.

## Slide 6: Types of Energy
It is important to note that the total energy in a system never changes (the law of conservation of energy).
That is to say, there must be the same total energy at the end of a vessel as there is at the beginning.
However, the types of energy may be different between the two points.
For example, potential energy may be the predominant type of energy at the beginning of a vessel, but it is typically converted to kinetic energy and heat (from friction) as the blood travels through the cardiovascular system.
The kinetic energy plus the heat energy is equal to the potential energy that was initially found at the beginning of the vessel.

## Slide 7: Pressure Gradient
Flow is the volume of blood moving through a vessel per unit time.
In order for there to be flow, there must be higher pressure at one end of a blood vessel and lower pressure at the other end.
This variance in pressure is referred to as a pressure gradient.
The amount of flow in a blood vessel is directly proportional to the pressure gradient.
Therefore, the bigger the difference in pressures, the more flow that occurs.

## Slide 8: Pressure Gradient
The systemic circulation begins with the left ventricle of the heart to the aorta, and from the aorta to the arteries of the body.
The arteries become arterioles, the vessels responsible for vasoconstriction and vasodilatation in the body.
Arterioles become the capillaries, where nutrient and waste exchange occurs.
From the capillaries, the blood flows into the venules and then into the veins.
The venous part of the systemic circulation is known forits capacitance, as approximately 2/3 of the blood is stored in the veins.
The veins drain into the inferior vena cava or superior vena cava, both of which empty into the right atrium.

## Slide 9: Blood Vessels and Blood Flow

## Slide 10: Structure of Blood Vessels
Blood vessels are made up of muscle that enables them to expand or contract as needed.
The walls of the arteries and veins are similar in that they consist of the same layers.
Both arteries and veins have a tunica intima, tunica media, and tunica adventitia.
The inner layer of the vessel, the layer closest to the flowing blood, is the tunica intima.
The outer layer is referred to as the tunica adventitia or externa.
This layer requires its own source of blood.
The vasa vasorum, a small network of blood vessels, accomplishes this task.

## Slide 11: Structure of Blood Vessels
Between the intima and adventitia is the middle muscular layer, the tunica media.
It is this layer of muscle and elastic tissue that differs dramatically between veins and arteries.
As blood travels through the cardiovascular system, the arteries and veins experience differences in pressure.
Arteries are unique in that they experience a pressure wave as blood is pumped from the heart.
One can feel this pressure wave as a “pulse” within the arteries as the heart beats.
It is because of this pressure that arteries typically have a much thicker tunica media compared with veins.

## Slide 12: Types of Blood Flow
Three types of flow are found in blood vessels: plug flow, laminar flow, and turbulent flow.
Plug flow can be found in large blood vessels such as the ascending aorta and at the entrance of vessels such as the common carotid artery.
The velocity profile of plug flow is blunt as a result of the flow traveling at the same velocity.

## Slide 13: Types of Blood Flow
Turbulent flow results when the red blood cells become chaotic and disorganized, resulting in an assortment of velocities.
Nonetheless, turbulent flow does not always indicate the presence of pathology.
At some points in normal vessels, such as in the area of the carotid bulb, turbulence can be found.

## Slide 14: Types of Blood Flow
Turbulence may also occur from high-velocity flow and from tortuous or kinked vessels.
The equation used to quantify the degree of turbulence in a blood vessel is the Reynolds number.
A Reynolds number greater than 2000 is considered to represent true turbulence.

## Slide 15: The Continuity Equation and Bernoulli’s Principle
As blood flows through the body, it may encounter vessels that have a decreased radius, possibly secondary to stenosis caused by thrombus.
When blood flows through an area of decreased radius, the same amount of flow must travel through that area.
The continuity equation ties together the relationship between the vessel area, the velocity of blood, and the volume of blood flow.
The volume of liquid that enters a blood vessel must be the same at any point along the length of the blood vessel.

## Slide 16: The Continuity Equation and Bernoulli’s Principle
Blood flow is constant.
Therefore, if the area of the vessel decreases, as in the case of a stenosis, the velocity must increase.
Bernoulli’s principle states that an increase in velocity must be accompanied by a corresponding decrease in pressure.

## Slide 17: The Continuity Equation and Bernoulli’s Principle
This inverse relationship between pressure and velocity is linked to the law of conservation of energy.
Subsequently, any increase in velocity is an increase in energy, and therefore something (the pressure) must decrease to preserve the total energy.
Once the vessel goes back to its prestenotic area, there is a decrease in velocity with a corresponding increase in pressure.

## Slide 18: Poiseuille’s Law
In addition to the pressure differential, there are other factors that may increase or decrease the amount of blood flowing through a blood vessel, including the length of the vessel, the radius of the vessel, and the viscosity of the blood.
These factors are all tied together by an equation known as Poiseuille’s law.
Poiseuille’s law describes the relationship between the volume of blood flow and the resistance to flow in a blood vessel.

## Slide 19: Poiseuille’s Law
Essentially, the law states that flow is equal to the difference in pressure divided by the resistance to flow in the vessel.
If the length of the vessel or the viscosity of the blood (both of which contribute to resistance to flow) increases, there is decreased flow.
Likewise, if the radius of the vessel increases, flow increases.
In fact, if the radius doubles, flow increases by a factor of 16.
In summary, an increase in length or viscosity decreases flow, while an increase in radius increases flow.

## Slide 20: Poiseuille’s Law
Inertial losses occur as vessels branch and change direction.
Friction, another form of resistance, is the loss of energy in the form of heat and is another detriment to flow.
As the arterioles branch out into capillaries, frictional and inertial losses are responsible for the accompanying decrease in the velocity of the blood.

## Slide 21: Poiseuille’s Law
The capillaries are tiny, typically about the width of a red blood cell.
It is the small size of the capillaries that contributes to the energy loss and slow velocity of flow.
However, this slow flow is essential for the function of the capillaries, which is the exchange of nutrients and waste products.

## Slide 22: Poiseuille’s Law
Poiseuille’s law assumes a straight (noncurved), rigid (nonelastic) pipe with a steady flow rate (nonpulsatile). Unfortunately, this does not describe the blood vessels found in the human body.
Although there is no simple way to describe the cardiovascular system, Poiseuille’s law demonstrates the relationships of flow and resistance.
Poiseuille’s law is analogous to Ohm’s law, a principle in electronics in which flow is equal to the pressure differential divided by resistance.

## Slide 23: Resistance and Stenotic Flow
The theorems provided by Bernoulli and Poiseuille describe the energy losses and changes in energy that occur as blood travels.
It has been previously described that flow is a constant and does not change.

## Slide 24: Resistance and Stenotic Flow
Said another way, the heart continues to beat and pump the same volume of blood regardless of the presence of a stenosis downstream.
However, there can be a stenosis so severe that it compromises flow to a certain part of the body.

## Slide 25: Resistance and Stenotic Flow
A critical stenosis, also referred to as a hemodynamically significant stenosis, is one in which there is decreased distal flow.
This situation would lead to a significant pressure gradient.
A cross-sectional area loss of 75% is generally considered to be hemodynamically significant, though this percentage may vary among vessels.
It is important to remember that a 75% decrease in area corresponds to a 50% decrease in diameter.

## Slide 26: Resistance and Stenotic Flow
Blood vessels may be connected end to end (in series) or flow into multiple parallel channels (in parallel).
The effective resistance, the resistance of the distal bed, is the sum of the individual resistances when multiple vessels are connected in series.
When vessels are connected in parallel, the effective resistance is reduced, as there are more channels or paths for flow to exploit.

## Slide 27: Resistance and Stenotic Flow
Arterioles, because of their muscular walls, are the main contributors to the resistance in the cardiovascular system.
The innervated arteriole walls can constrict or dilate in response to signals from the brain to either increase or decrease flow distally.
At the region of a nonhemodynamically significant stenosis, the velocity of the blood cells must increase in order to maintain the same volume flow.

## Slide 28: Resistance and Stenotic Flow
The area of increased velocity is accompanied by a decrease in pressure through this region, as described by Bernoulli’s principle.
As the blood exits the region of narrowing and enters a suddenly expanded vessel, there is turbulence as the blood spills out.
This turbulence eventually dissipates and downstream the flow returns to its previous prestenotic state.

## Slide 29: Resistance and Stenotic Flow
Another important hemodynamic concept to grasp is that with a stenosis, it is more detrimental to have more than one stenosis in a vessel than a single substantial lesion.
This is true because there is more energy loss with two stenoses in series. This concept relates to what happens with vessels connected in a series, in which the total resistance is the sum of the segmental resistances.

## Slide 30: Resistance and Stenotic Flow
Because a decrease in radius causes increased resistance to flow, there is an increase in total resistance when there is more than one stenosis in a vessel.
Therefore, it is possible that multiple nonhemodynamically significant lesions will act as a critical lesion.

## Slide 31: Resistance and Stenotic Flow
It is vital to recognize that blood will always follow the path of least resistance.
In the body, if a major artery is blocked it becomes the path of highest resistance, while the previously collapsed collaterals become the path of least resistance.
The higher pressure proximal to a stenosis causes the collaterals to open up and the blood follows the lower-resistance path.

## Slide 32: Resistance and Stenotic Flow
Distal to the stenosis, the collateral eventually rejoins the main artery. In chronic disease, if the collateral network is extensive enough, the net flow distal to the stenosis may actually be normal.
Collaterals are formed over time and in response to chronic change.
They are typically not found in the presence of an acute obstruction.

## Slide 33: Venous Hemodynamics and Hydrostatic Pressure
As flow leaves the capillaries, it enters the larger venules.
The veins that are located between the capillaries and the right atrium of the heart get progressively wider, thus offering lower resistance to flow.
The pressure in the venules is very low, about 15 millimeters of mercury (mm Hg), but still higher than the pressure in the right atrium, which is typically 0 to 8 mm Hg.

## Slide 34: Venous Hemodynamics and Hydrostatic Pressure
Assuming that the person is supine, this small, but still significant difference in pressure is a pressure gradient, and therefore, there exists forward flow (toward the heart).

## Slide 35: Venous Hemodynamics and Hydrostatic Pressure
When someone is in the standing position, gravity acts on the blood in the form of hydrostatic pressure.
As mentioned earlier, hydrostatic pressure is the weight of a column of fluid from a certain reference point.
In humans, that reference point is the heart, the point at which the hydrostatic pressure is zero.
Below the heart, the weight of this column of blood increases with the distance from the heart.

## Slide 36: Venous Hemodynamics and Hydrostatic Pressure
Blood in a vertical tube acts in the same way. That is, the farther from the heart, the more weight there is to support.
Therefore, the highest hydrostatic pressures are located at more distal parts of the body, such as the feet and ankles.
Hydrostatic pressure is the reason that venous stasis ulcers are found at the ankles and not in the thighs.

## Slide 37: Venous Hemodynamics and Hydrostatic Pressure
Recall that hydrostatic pressure can be calculated by using the density of the blood, gravity, and the height at which you are measuring, or distance from the heart.
Notice in the formula that the height variable is the only variable that is not a constant.
If the point at which you are measuring is below the heart, the hydrostatic pressure will be positive.

## Slide 38: Venous Hemodynamics and Hydrostatic Pressure
Conversely, if a point is measured above the heart, such as an outstretched arm over the head, the hydrostatic pressure will be negative.

## Slide 39: Venous Hemodynamics and Hydrostatic Pressure
Appropriate venous return to the heart requires several mechanisms to work properly.
First, as mentioned earlier, a pressure gradient exists between the venules and the right atrium.
Second, with inspiration an area of low pressure is formed within the thorax, causing the blood to be forced into the chest.

## Slide 40: Venous Hemodynamics and Hydrostatic Pressure
Third, venous valves, folds of endothelial tissue inside of the veins, provide a method to ensure forward flow by only permitting the flow of blood in one direction, to the heart. The calf muscle pump provides the final mechanism.
The soleal sinuses inside the calf muscle store venous blood.
When the calf muscles are used, blood is forced into the veins.

## Slide 41: Venous Hemodynamics and Hydrostatic Pressure
There is not only pressure inside the veins, but outside the veins as well in the form of extrinsic pressure.
Transmural pressure is the difference between the pressure inside the vein (intravascular pressure) and the surrounding tissue.

## Slide 42: Venous Hemodynamics and Hydrostatic Pressure
With low transmural pressure, which may occur when a patient is lying supine, the force outside the vein exceeds the pressure inside the vein and the vein collapses and has an elliptical shape.
When the patient stands and the hydrostatic pressure increases, the transmural pressure increases and the vein assumes a circular shape.

## Slide 43: Venous Hemodynamics and Hydrostatic Pressure
Flow in the veins should not be pulsatile, with the exception of the systemic veins in close proximity to the heart.
Rather, veins should be phasic or show variations that relate to respiration.

## Slide 44: Venous Hemodynamics and Hydrostatic Pressure
Pulsatility in the peripheral veins may indicate trouble with the right side of the patient’s heart and should be documented.
Lack of respiratory phasicity, referred to as “continuous flow,” may be an indicator of intrinsic thrombus or extrinsic compression between the vein being sampled and the heart, and should also be documented.

## Slide 45: Pulsatility and Phasicity
Unlike veins, arteries should be pulsatile in nature, with a distinct systole and diastole that correspond to both the flow from the heart and to the distal vascular bed.
Flow is often described by the shape of its waveform on spectral Doppler as triphasic, biphasic (collectively known as “multiphasic”), or monophasic.
Flow that is triphasic or biphasic feeds a high-resistance bed, and there is typically little diastolic flow evident, with possibly some flow reversal in diastole.
Monophasic flow feeds a low-resistance bed.

## Slide 46: Pulsatility and Phasicity
A low-resistance bed is a bed that demands constant flow in all phases of the cardiac cycle.
Examples of a low-resistance bed are the internal carotid artery (ICA), which feeds the brain, and the renal artery that supplies the kidney.
The shape of the waveform may be an indicator of disease that is more distal or more proximal to the sampling point.
In the presence of a proximal stenosis, the distal arterioles will dilate, thereby allowing more oxygenated blood to get to the periphery.

## Slide 47: Pulsatility and Phasicity
The increase in diameter of the vessels is accompanied by a pressure drop.
For example, the lower extremity arteries are normally high-resistance vessels.
If there is a superficial femoral artery (SFA) obstruction, there will be dilatation of the distal arterioles, with a corresponding change to monophasic flow in the spectral waveform of the SFA.

## Slide 48: Pulsatility and Phasicity
Arterial phasicity is always about the resistance in the distal bed.
For example, in the resting patient, monophasic flow is always abnormal in the lower extremities.
If monophasic flow is seen in the lower extremity arteries of the resting patient, it indicates persistent dilation downstream, an abnormal condition.

## Slide 49: Pulsatility and Phasicity
Conversely, blood vessels that normally have low-resistance waveforms, such as the ICA, should never exhibit a high-resistance pattern.
If high-resistance flow is noted in the ICA, it would be an ominous sign indicating a distal high-pressure state, as seen with distal occlusion or near occlusion, cerebral edema, or brain death.

## Slide 50: Pulsatility and Phasicity
An additional noteworthy waveform shape that can be indicative of pathology is tardus parvus (“slow small”), which is seen in the presence of a proximal obstruction.
Tardus parvus waveforms are identified by a delay in the upstroke of the systolic component of the waveform (time-to-peak).
Most arteries have flow that initially accelerates rapidly, causing a sharp systolic upstroke.

## Slide 51: Pulsatility and Phasicity
An increased acceleration time, represented by a delay in the systolic upstroke, is a sign that there is an obstruction, and that obstruction is located more proximal to the point of sampling.
It is important to remember that a proximal obstruction causes distal arteriolar dilation; therefore, tardus parvus waveforms are monophasic in nature.
Tardus parvus waveforms always indicate that there is an obstruction proximal to the point of sampling.

## Slide 52: Effects of Exercise on Flow
In the resting patient, the peripheral lower extremity arteries are normally of high resistance due to distal arteriolar constriction.
With exercise, there is an increased demand for oxygen by the muscles.
This increase in demand causes arteriolar dilation, which results in larger-diameter blood vessels, and therefore a lower-resistance distal bed with a corresponding increase in blood flow.

## Slide 53: Effects of Exercise on Flow
In the normal patient, there is little pressure change in the distal lower extremities as a result of this arteriolar dilation.
The patient with arterial obstructive disease may have normal resting pressures, but the increased demand for oxygen that occurs with exercise may be more than the blood vessels are able to supply, causing a pressure drop distally.

## Slide 54: The Doppler Effect
The effect of differing frequencies with motion was first noted by Christian Doppler and is thus called the Doppler effect.
Doppler discovered that when sound impinges on a stationary reflector, the reflected frequency is identical to the transmitted, or incident, frequency.
However, when a reflector is moving toward the transducer, the reflected frequency will be higher than the transmitted frequency.
Likewise, when a reflector is moving away from the transducer, the reflected frequency will be lower than the transmitted frequency.

## Slide 55: The Doppler Effect
The difference between the transmitted and reflected frequencies is called the frequency shift, or Doppler shift.
A positive frequency shift occurs when a reflector is moving in a direction that is toward the transducer.
A negative frequency shift occurs when a reflector is moving in a direction that is away from the transducer.
The frequency shift can be calculated by utilizing the Doppler equation.

## Slide 56: The Doppler Effect
When the transmitted frequency is subtracted from the reflected frequency, the result is a number that is approximately 1/1000th of the operating frequency.
The resultant value is in the audible range of sound, meaning that all that is needed to hear the frequency shift is a set of speakers or headphones.
If the resultant value is a positive number, then there is a positive shift and flow is moving toward the transducer.
Likewise, if the resultant value is a negative number, then there is a negative shift and flow is moving away from the transducer.

## Slide 57: The Doppler Effect
While the frequency shift is measured by the machine, it is the velocity of the blood that is of interest to the imager, and not the frequency shift itself.
The ultrasound system measures the frequency shift but calculates the velocity.

## Slide 58: The Doppler Effect
Doppler works because the incident sound reflects off of the red blood cells in the blood. Red blood cells are small, normally about 7.0 μm.
Because of their size, they are natural Rayleigh scatterers.
Rayleigh scatterers are very small compared with the incident wavelength.
As frequency increases, the intensity of scatter increases proportional to the fourth power of the frequency; therefore, a small increase in frequency results in a dramatic increase in scatter.

## Slide 59: The Doppler Effect
Higher-frequency transducers may provide stronger Doppler signals, but at the expense of the attenuation.
Therefore, the higher the frequency, the more scatter there is, and therefore, the more attenuation.
Remember that scatter is a form of attenuation.
Therefore, if the energy is scattered, it is not transmitted deeper into the tissue.
Essentially, there has to be a trade-off between improved resolution and penetration.

## Slide 60: The Doppler Effect
In the Doppler equation, it is not the Doppler angle that is utilized in the equation, but rather the cosine of the angle.
As the Doppler angle increases, the cosine of the angle decreases.
That is, the Doppler angle and the frequency shift are inversely proportional.
The Doppler angle must be known in order to accurately calculate the velocities, although in echocardiography a 0° angle is always assumed.

## Slide 61: The Doppler Effect
The most accurate Doppler shift (and therefore the most accurate velocity) will come from a 0° angle.
Because of the inverse relationship between the Doppler angle and the cosine of the angle, as the angle increases the frequency shift decreases.
Therefore, the highest Doppler shift comes from a 0° angle.
No Doppler shift is obtained at a 90° angle; at an angle of 90°, the cosine of 90 is 0, and therefore, the Doppler shift is 0.

## Slide 62: The Doppler Effect
Some Doppler devices are nondirectional, or unable to distinguish between positive or negative Doppler shifts.
In order to determine the direction of flow, Doppler devices use phase quadrature to determine whether there is a positive shift, flow toward the transducer, or a negative shift, flow away from the transducer.
Phase quadrature permits bidirectional Doppler, which is able to display positive versus negative shifts.
There are two ways of obtaining a Doppler signal: continuous-wave (CW) and pulsed-wave (PW).

## Slide 63: Continuous-Wave Doppler
A continuous-wave (CW) Doppler device consists of two elements. One element is used by the system to constantly transmit sound and the other is used to constantly receive sound.
CW devices are constructed this way because the piezoelectric elements used by the system to create ultrasound cannot send and receive at the same time.

## Slide 64: Continuous-Wave Doppler
CW devices do not pause to listen for the return echo, nor do they calculate how long it takes for the echo to return.
Therefore, CW devices have no range resolution, or the ability to determine how far away the reflectors are from the transducer. It is for this reason that CW transducers themselves do not provide a 2D image, only a spectral Doppler waveform.

## Slide 65: Continuous-Wave Doppler
The sample volume, or region that is being measured by Doppler, is very large with CW Doppler.
Any blood vessel that lies within the sample volume will be measured and displayed in the signal.
With CW Doppler, the operator is not able to select a specific vessel.
This dilemma can present problems when there are several vessels within the sample volume.

## Slide 66: Continuous-Wave Doppler
The CW transducer is driven by an oscillator that provides a continuous voltage to the transmitting element.
With CW transducers, the oscillating voltage is equal to the operating frequency.
If the oscillator vibrates at 3,000,000 times per second, the CW transducer operates at 3 MHz.

## Slide 67: Continuous-Wave Doppler
The signal processor in the machine compares the transmitted and received frequencies, and their difference is sent to a loudspeaker and/or spectrum analyzer.
There is no damping with a CW transducer; if the sound is being transmitted continuously, damping is not needed.
The continuously transmitting CW device has a 100% transmit time.
Therefore, the duty factor of a CW device is 100%, or 1.

## Slide 68: Analyzing the Spectral Waveform
The signal that is received by the transducer is a complex mix of frequency shifts and time.
The signal undergoes processing before it is displayed to improve the analysis of Doppler information.
Spectral analysis dismantles the complex signal and breaks it down by frequency.
The resultant waveform is a visual, quantifiable representation of what is happening in the blood vessel at a given point in time.

## Slide 69: Analyzing the Spectral Waveform
The mathematical technique used to break down the signal and produce a spectral waveform is called Fast Fourier Transform (FFT).
Accurate velocity measurements are needed to be able to quantify the level of disease and perform other assessments, and it is FFT that accomplishes this task.
The spectral display provides the following information: time, velocity, frequency shift, flow direction, and amplitude.

## Slide 70: Analyzing the Spectral Waveform
Time is displayed on the spectral display along the x-axis.
Tick marks represent seconds, so it is possible to calculate events as they occur over a specific period of time.
The number of seconds displayed at one time can be adjusted by changing the sweep speed of the Doppler instrument.

## Slide 71: Analyzing the Spectral Waveform
As stated earlier, it is the frequency shift that is measured by the machine; however, it is the velocity information that is of most interest.
Therefore, today’s spectral displays commonly display only velocity information.
On some machines, it may be possible to also display frequency shift information, but to reduce interoperator variability, angle-corrected velocities are commonly used (except in echocardiograph and transcranial Doppler which do not use angle correction).

## Slide 72: Analyzing the Spectral Waveform
Measurement of the flow velocity enables the sonographer to measure peak systolic and end diastolic measurements, which are, in turn, used to quantify the degree of disease within vessels.
In addition to the peak systolic and end diastolic velocities, the mean velocity is used for some applications.

## Slide 73: Analyzing the Spectral Waveform
The mean velocity is derived by tracing the spectral waveform from end diastole of one heartbeat to end diastole of the next heartbeat.
Examples of measurements that are obtained on a spectral waveform include the resistive index (RI) and the pulsatility index (PI).
The RI is used to quantitate the resistiveness of the distal vascular bed.

## Slide 74: Analyzing the Spectral Waveform
An example of the use of RI is for the analysis of the kidneys in cases of hydronephrosis.
The PI is used to determine how pulsatile a vessel is over time.
The PI is often used in obstetrics in evaluation of fetal brain and umbilical cord.
Both of these measurements endeavor to estimate the relative difference between systole and diastole.

## Slide 75: Analyzing the Spectral Waveform
Flow direction is displayed on the spectral display as flow being above or below the baseline.
Flow on one side of the baseline is a “positive shift” and flow on the other side represents a “negative shift.”
The flow can be inverted for convention so that flow always appears above the baseline, even when it represents a negative shift.

## Slide 76: Analyzing the Spectral Waveform
The spectral display also allows for display of pathologic reversal of flow.
Reversal of flow may occur in the ICAs when cerebral edema is present, or in the fetal umbilical artery when there is severe placental insufficiency.
When trying to determine whether the flow is “toward” or “away” from the transducer, the practitioner must search for the minus (negative) sign that precedes the velocity on the spectral velocity chart.
Some machines display “INVERTED” instead of a minus sign to denote that the display has been inverted.

## Slide 77: Analyzing the Spectral Waveform
The amplitude of the signal is represented by the brightness of the dots on the spectral display, the so-called z-axis.
The brighter the dots of the spectral waveform, the more red blood cells that make up the signal.
The envelope of the waveform represents how many red blood cells are traveling at that velocity at a specific period in time.

## Slide 78: Analyzing the Spectral Waveform
The wider the range of velocities in a sample in a given point of time, the thicker the envelope.
In a normal vessel, a small sample volume is typically used in order to sample only the highest velocities in the center of the vessel.
A large sample volume that encompasses both the fast central flow and all the progressively decreasing velocities toward the edges will represent many different velocities.
The area under the envelope is called the spectral window.

## Slide 79: Analyzing the Spectral Waveform
A flow sample in which the red blood cells are traveling at almost identical speeds, as in the case of laminar flow with a small sample volume, will demonstrate a thin envelope.
Conversely, only analyzing one instance of time in turbulent flow or utilizing when a large sample volume is used will demonstrate a wide range of velocities.
This turbulent flow therefore demonstrates a filling-in of the spectral envelope. This is termed spectral broadening.

## Slide 80: Analyzing the Spectral Waveform
As mentioned earlier, turbulence is not always pathologic.
Turbulence is normal and expected in some instances, such as in the area of the carotid bulb.
However, if turbulence is seen where one expects to see laminar flow, further investigation is warranted.
The spectral window disappears in the presence of spectral broadening.
CW flow uses a large sample volume and samples many vessels (at a variety of velocities) at the same time.
Therefore, CW waveforms will typically demonstrate spectral broadening.

## Slide 81: Pulsed-Wave Doppler
Pulsed-wave (PW) Doppler functions much like PW grayscale imaging in that it transmits pulses of sound and waits for the sound to return in order to determine the depth of the returning echoes.
Unlike CW, PW Doppler allows the operator to select the depth at which the Doppler measurements will be taken.
The operator places a range gate over the vessel to be sampled, and the area within that gate, the sample volume, is where the PW Doppler signal is obtained.
The operator can select the size of the sample volume by adjusting a “gate” control on the machine, which permits many different size sample volumes.

## Slide 82: Pulsed-Wave Doppler
Grayscale devices typically use 2 to 3 cycles per pulse to produce a B-mode image.
PW Doppler devices typically transmit anywhere from 5 to 30 cycles per pulse.
This higher pulse length provides a more accurate sampling of the blood.
PW Doppler also utilizes angle correction. Angle correction is used with PW Doppler in order to more accurately calculate the velocities from the frequency shifts.

## Slide 83: Pulsed-Wave Doppler
When performing Doppler studies, it is rare that the transducer is parallel to the flowing blood.
Therefore, angle correction is used to inform the machine what the flow angle is, so that velocities can be accurately calculated.

## Slide 84: Pulsed-Wave Doppler
PW Doppler devices also permit duplex imaging where the B-mode image is on the display at the same time as the Doppler signal.
Duplex imaging allows for real-time adjustment of the Doppler cursor while observing the grayscale image.
With duplex imaging, the Doppler and 2D information must be obtained separately.

## Slide 85: Pulsed-Wave Doppler
The acquisition of the grayscale information alternates with obtaining the Doppler information.
This switching back and forth occurs very fast but does affect the frame rate in a negative way, because it decreases the temporal resolution.
Triplex imaging is combined grayscale, spectral, and color Doppler information on the screen.

## Slide 86: Pulsed-Wave Doppler
PW Doppler has a major limitation called aliasing. Aliasing is a wraparound of the Doppler signal, where the positive shifts are displayed as negative shifts.
The highest frequency shift that can be measured is equal to one half the pulse repetition frequency (PRF), which is known as the Nyquist limit. PRF is the number of pulses per second.

## Slide 87: Pulsed-Wave Doppler
For example, if the PRF is 2500 Hz, a Doppler shift of 1250 Hz or greater will alias.
Aliasing occurs because the Doppler signal must be measured at such a rapid rate.
If the PRF is too low, as in the case of a deep blood vessel, the blood cannot be sampled fast enough, and the signal is displayed erroneously.
In order to eliminate aliasing, either the PRF needs to increase or the Doppler shift needs to decrease.

## Slide 88: Review of Doppler Controls
Numerous controls are used to manipulate the spectral waveform to aid in diagnosis and interpretation.
The range gate, already mentioned in previous sections, is the cursor used in PW Doppler that is placed in the vessel where sampling is desired.
The size of the sample volume may be controlled by increasing or decreasing the size of the gate.

## Slide 89: Review of Doppler Controls
With CW Doppler, the sampling depth cannot be selected. However, there is a cursor that is placed over the area to be sampled.
The sample volume, which is not user controllable with CW Doppler, is larger than PW Doppler and may encompass several blood vessels.

## Slide 90: Review of Doppler Controls
Angle correction is used with PW Doppler in order to more accurately calculate the velocities from the frequency shifts.
The higher the Doppler angle, the greater the degree of potential error in the measurement.
Angles greater than 60° exhibit a very high rate of velocity measurement error, and therefore should be avoided.
When using a linear transducer, the Doppler cursor can be steered to either the left or the right.

## Slide 91: Review of Doppler Controls
Some machines enable the operator to specify the angle of the steer.
The advantage of this is that it permits the operator to keep the angle correction at or below 60° by changing the steer angle.
In transducers where the steer angle itself cannot be adjusted, the operator may have to “heel” or “toe” the transducer in order to angle correct.
The operator must always try to avoid a 90° angle to flow when sampling a vessel.

## Slide 92: Review of Doppler Controls
The scale, or PRF setting on the machine, is the sampling rate of the Doppler.
The sampling rate has to be fast enough in order to accurately plot the frequency shifts or aliasing will occur. The PRF is determined by the depth.
The deeper the vessel, the lower the PRF, and subsequently the higher the risk of aliasing.

## Slide 93: Review of Doppler Controls
Likewise, when sampling vessels with high frequency shifts (velocities), the PRF needs to be increased to keep sampling at an adequate rate.
If the frequency shift is greater than one half of the PRF (the Nyquist limit) then aliasing will occur.
When sampling vessels with slow or hard-to-find flow, the PRF needs to be decreased in order to make the waveform bigger on the screen.
A small waveform is poor technique and does not allow for accurate measurements, when needed.
Typically, the spectral waveform should occupy two thirds of the spectral display window.

## Slide 94: Review of Doppler Controls
Occasionally, when a deep vessel needs to be imaged the PRF cannot sample at a sufficient rate.
Some ultrasound systems solve this dilemma with the use of a high PRF (HPRF) setting, which allows the machine to ignore the depth ambiguity problem.
When the machine goes into HPRF mode, multiple range gates appear on the screen signifying that the machine is not sure where the pulse is coming from, and could have originated from anywhere along the Doppler cursor.

## Slide 95: Review of Doppler Controls
The wall filter is a Doppler control used to eliminate the low-frequency signals caused by wall or heart valve motion.
Movement of the heart or vessel walls causes a low-frequency, high-amplitude signal that appears on the spectral display as low-level acoustic noise, or clutter.
Noise takes away from the image and does not contribute useful information and is therefore filtered out with the wall filter.

## Slide 96: Review of Doppler Controls
Other names for the wall filter are high-pass and wall-thump filter. In general and vascular imaging, wall motion is not a concern, so the wall filter is kept low.
In cardiac imaging, a high wall filter is used to counteract the signal coming from the movement of the myocardium and valves.
Caution should be used when applying the wall filter so that useful diastolic information is not removed from the spectral display.

## Slide 97: Review of Doppler Controls
The gain of the spectral display can be set independent of the grayscale gain.
The brightness of the dots of the spectral display corresponds to the amplitude of the Doppler shift.
If the spectral signal is weak, the gain can be increased to improve visualization of the signal. If the spectral gain is too high, it may cause over measurement of the spectral waveform, so it is imperative that the gain be set to an appropriate level.

## Slide 98: Review of Doppler Controls
The baseline, the movable dividing line between positive and negative frequency shifts, is typically set near the bottom of the spectral display window.
However, it should not be set all the way at the bottom of the display or aliasing may be overlooked.

## Slide 99: Review of Doppler Controls
Aliasing may be seen if the baseline is too high as well.
Lowering the baseline will resolve this problem.
Unfortunately, lowering the baseline may eliminate the appearance of aliasing; but, if the Doppler shift is greater than the Nyquist limit, aliasing is still present even if lowering the baseline appears to eliminate the problem.

## Slide 100: Color Doppler Imaging
Color Doppler imaging (CDI), a PW technique, is a color representation of the Doppler shift information superimposed on the grayscale image.
CDI provides information pertaining to both the direction and mean velocity of the flow.

## Slide 101: Color Doppler Imaging
Autocorrelation is the processing technique used to obtain the color flow information, but because it is relatively fast, it is not as accurate as FFT.
CDI only provides the mean velocity information and not maximum velocities.

## Slide 102: Color Doppler Imaging
CDI also uses a larger gate than spectral Doppler, a gate that is made up of many scan lines proportional to the width of the gate.
Color information is obtained at many points along each scan line and each pulse packet is checked for movement, opposed to nonmovement, by searching for frequency shifts.
Moving reflectors are specified as a color and nonmoving reflectors are specified as a shade of gray.

## Slide 103: Color Doppler Imaging
The ensemble length, also known as the packet size, is the number of pulses per scan line within the color gate.
The higher the ensemble length, the more sampling points along each scan line, and therefore, the higher the sensitivity of the color signal.
High ensemble lengths increase the ability to detect slow flow and offer a more accurate mean velocity.
Unfortunately, this is at the expense of the frame rate, which is very low with high ensemble lengths.

## Slide 104: Color Doppler Imaging
The ensemble length can be as low as 3 pulses per scan line but is typically around 10 to 20 pulses per scan line.
Another disadvantage of high ensemble lengths is the machine’s inability to detect rapidly changing hemodynamic events secondary to the longer acquisition time.
CDI is inherently slow, and large gates and/or high ensemble lengths slow it down even further.
For the best frame rate, the smallest color gate should always be employed.

## Slide 105: Color Doppler Imaging
The color Doppler scale shows direction of flow as a color or range of colors on each side of a black baseline.
Black within a color display means that either there was no Doppler shift present in that location (as a result of either a 90° angle to flow or no flow), or the shift was so low that it was eliminated by wall filters.
In general and vascular imaging, the color scale is often set by convention, so that red represents arteries and blue represents veins.

## Slide 106: Color Doppler Imaging
In cardiac imaging, the color scale is thought of as BART: blue away, red toward.
However, the color scale can be inverted, so that blue is toward and red is away.
The preferred color scale setting may vary from lab to lab.

## Slide 107: Color Doppler Imaging
The color scale is most commonly presented in velocity mode, where the colors are vertically oriented for positive/negative shifts.
Another mode, associated with cardiac imaging, is variance mode, where colors are represented vertically and shades of green are oriented horizontally to denote the presence of turbulence.
There are three main components of the color imaging: hue, saturation, and brightness (or luminance).

## Slide 108: Color Doppler Imaging
The hue of a color is the color itself as determined by its wavelength.
A color can be made to appear lighter by adding white to it.
Saturation is how much white is added compared to the original color.

## Slide 109: Color Doppler Imaging
The less white in the color, the more saturated it is.
Pink, for example, is less saturated than red.
The brightness of the color is how intense the color is and related to the amplitude of the signal.
One of the more challenging aspects of CDI is identifying direction of color flow just by looking at the image and the color scale.

## Slide 110: Color Aliasing
As a PW technique, CDI is bound by the same limitation as PW spectral Doppler.
Therefore, aliasing can occur.
Aliasing on CDI is represented by a wraparound of the color scale.
As with spectral Doppler, aliasing can be eliminated by increasing the PRF/scale.
Appropriate setting of the color PRF allows for setting the proper sensitivity to flow.

## Slide 111: Color Aliasing
Low PRF color settings are used for slow or difficult-to-demonstrate flow, and high PRF settings are used for fast flow and also to eliminate aliasing.
In addition to PRF, color Doppler also has a gain setting, and it is imperative that the gain is set properly.
If the color gain is set too high, the result is color noise throughout the color gate.
If the color gain is set too low, the vessel will not be adequately filled with color.

## Slide 112: Color Aliasing
In the presence of very slow flow, or if small vessels are being analyzed, it may be helpful to average multiple frames instead of displaying only one frame of color information at a time.
Increasing the persistence setting reduces the effect of noise and makes it easier to follow small vessels.
The trade-off of high persistence is a decrease in the frame rate.
When both grayscale and color information are present within the same pixel, color priority is a setting on the machine that allows the operator to set a threshold for displaying color pixels instead of grayscale pixels.

## Slide 113: Color Aliasing
A pixel, the smallest component of an ultrasound image, can either be a color or shade of gray, not both at the same time.
Priority sets the threshold that the amplitude (i.e., brightness of the shade of gray) will have to exceed in order for grayscale pixels to be displayed rather than color pixels.

## Slide 114: Color Aliasing
Below that threshold, color pixels will be placed. If the priority is set too low, then image noise or artifacts within the vessel will be displayed instead of color pixels.
A higher priority setting is useful in filling a vessel with color when there is a low signal-to-noise ratio.

## Slide 115: Tissue Doppler Imaging
Specifically used for cardiac imaging, tissue Doppler imaging (TDI) is another CDI technique.
Flowing blood typically produces a low-amplitude, high-velocity signal.
However, myocardial wall motion produces a high-amplitude, low-velocity signal. Instead of using a high-pass filter to filter out the signal from the wall motion, TDI uses a low-pass filter to eliminate the signal from the blood and only show color information representing the wall motion.

## Slide 116: Tissue Doppler Imaging
TDI is still limited by frequency shifts at 90° angles; but since the myocardial walls are oriented 0° to the beam in some views, this is not a limitation.
TDI can be performed with color Doppler and spectral Doppler display modes.

## Slide 117: Power Doppler
PW spectral and color Doppler are limited by flow at 90° angles, because the frequency shift on which the flow information is based is equal to 0 at that critical angle.
Power Doppler, also termed color Doppler energy or power angio, ignores the frequency shift information and focuses only on the amplitude, or strength, of the shift.
Power Doppler is only able to display amplitude information and does not provide information on velocity or direction of flow.

## Slide 118: Power Doppler
Power Doppler is almost completely independent of angle, which makes it quite functional for evaluating slow flowing and/or tortuous vessels.
Both an advantage and a disadvantage of power Doppler is its sensitivity.
Since power Doppler is very sensitive, it is ideal for slow, small vessels, but it also makes it more susceptible to patient or organ motion.
Flash artifact occurs when power Doppler is being used and inadvertent motion interrupts the quality of the signal.

## Slide 119: Cardiac Strain and Strain Rate
Cardiac strain and strain rate are used for measuring myocardial function.
Strain is the changing of the shape of the muscle as it lengthens and contracts.
Strain and strain-rate analysis permit evaluation of the deformation of the cardiac wall to evaluate for ventricular function.
Speckle tracking is the method used to obtain the strain information.
By observing the “dots” that represent the myocardial tissue, the machine can measure the movement of the tissue in the longitudinal, radial, and circumferential axes.

## Slide 120: Doppler Artifacts
Table 4-24 provides a summary of several common Doppler artifacts and how to correct them.